## Slide 1: Finding the Dynamic Characteristics of a sensor
Vidhya Balaji

## Slide 2: Parameter Definition
Propagation Delay and Rise Time
Response Time
* ACS724KMA datasheet

## Slide 3: Block Diagram of Circuitry to produce sharp rise time signal
Gate Drive IC
Output pulse with 1 µsec or less rise time
Power resistor
Sensor DUT
GND
Current In
Current Out
GND
Sensor Output
Pulse generator

## Slide 4: Settings and Parameters
Signal Generator
  Pulse generated with rise time ~/< 1 µsec
Power MOSFET
  Powered with VDD >=10V, IDD ~ 10A or higher for output pulse of significant magnitude
  Preferably mounted on eval board with heat sink
Power resistor
  < 1 ohm, >25 W for maximum current throughput: Current ~ Voltage/R
  Smaller the R, greater the current
Oscilloscope
  Sample mode of acquisition
  HF reject
Common ground for all signals
VOUT (V)
Time (sec)
Output pulse from power MOSFET
Output pulse from sensor